## Slide 1
EXERCISE 1
Forward “Hello World” example
Aims:
Familiarise with FLEXPART structure and output
Set-up and execute a simple scenario
Plotting the output
Effect of the OUTGRID resolution
Effect of the number of particles
Questions? Write delia.arnold-arias@zamg.ac.at
Notes: 1
1

## Slide 2
#ifeq ($(gcc), 4.9)
# Compiled libraries under user ~flexpart, gfortran v4.9
# ROOT_DIR = /homevip/flexpart/
# F90 = ${ROOT_DIR}/gcc-4.9.1/bin/gfortran
# MPIF90 = ${ROOT_DIR}/bin/mpifort
# INCPATH1 = ${ROOT_DIR}/gcc-4.9.1/include
# INCPATH2 = ${ROOT_DIR}/include
# LIBPATH1 = ${ROOT_DIR}/lib
# System libraries at ZAMG, gfortran 4.9.2
F90 = gfortran
MPIF90 = mpif90
INCPATH1 = $(GRIB_API_INCDIR)
INCPATH2 = $(NETCDF_INCDIR)
LIBPATH1 = $(GRIB_API_LIBDIR)
LIBPATH2 = $(NETCDF_LIBDIR)
#else
# Compiled libraries under user ~flexpart, gfortran v5.4
# ROOT_DIR = /homevip/flexpart/
# F90 = /usr/bin/gfortran
# MPIF90 = /usr/bin/mpifort
# INCPATH1 = ${ROOT_DIR}/gcc-5.4.0/include
# INCPATH2 = /usr/include
# LIBPATH1 = ${ROOT_DIR}/gcc-5.4.0/lib
#endif
Compiling FLEXPART on ZAMG’s virtual machines
https://www.flexpart.eu
tar -xvf flexpart_v10.3.1_3cd0f17.tar
Edit makefile (see box to the left)
Compile: make serial
Edit par_mod.f90 (for ECMWF data):
integer,parameter :: nxmax=800,nymax=400,nuvzmax=138,nwzmax=138,nzmax=138, nxshift=0
integer,parameter :: maxnests=1,nxmaxn=800,nymaxn=400
integer,parameter :: maxpart=5000000
integer,parameter :: maxspec=10
LIBS = -lgrib_api_f90 -lgrib_api -lm -lnetcdff
LDFLAGS = $(FFLAGS) -L$(LIBPATH1) -Wl,-rpath,$(LIBPATH1) $(LIBS) -L$(LIBPATH2)
LDDEBUG = $(DBGFLAGS) -L$(LIBPATH1) $(LIBS) -L$(LIBPATH2)

## Slide 3
mkdir exercises  make the exercises folder
cd exercises  enter the exercises folder
mkdir Hello_World_fwd and cd Hello_World_fwd  make the directory for your hello world forward exercise
ln -s /path/to/metdata/ECMWF_meteorological_input/ ./ or ln -s /path/to/metdata/NCEP_meteorological_input/ ./
Some preparations… Preparing the structure
Find the necessary meteorological input data sets in “ECMWF_meteorological_input” and “NCEP_meteorological_input” for all the hands-on which path has to be entered in the respective pathnames file later on.
Meteorological files are heavy and it is best not to copy them in multiple places, linking is ideal.

## Slide 4
mkdir exercises  make the exercises folder
cd exercises  enter the exercises folder
mkdir Hello_World_fwd and cd Hello_World_fwd
ln -s /path/to/metdata/ECMWF_meteorological_input/ ./ or ln -s /path/to/metdata/NCEP_meteorological_input/ ./
Copy pathnames file and options folder from FLEXPART 10 folder. Pathnames file has to be edited accordingly for every exercise!
cd options Replace sub-folder SPECIES by ln -s /path/to/SPECIES/ ./
Link FLEXPART gfortran executable to working directory (i.e., Hello_World_fwd)
cp /path/to/plotting/plot_FLEX_binary.py ./
cp /path/to/plotting/read_header.py ./
cp /path/to/plotting/read_grid.py ./
9. mkdir output_[ECMWF,NCEP]
Remember steps 3 to 9 for all test cases!
Some preparations… Preparing the structure

## Slide 5
Hello World fwd & plotting
Specifications:
  COMMAND FILE:
    Forward run: 1 March 2007 9 am UTC to 2 March 2007 14 UTC
    Output every hour
    Convection
    Concentration output
    Nested output
    No adaptation to TL
  OUTGRID FILE:
    Resolution 0.1 degree
    LLC: 37.0°N, 0.0°E
    70 x 200 grid cells
    1 output layer, 250 m a.g.l.
This test case aims at making you run FLEXPART with a very simple case to warm-up for the following, more complicated FLEXPART options
  OUTGRID NEST
    Resolution 0.015
    420 x 220 grid cells
    LLC 37.5°N°E. 1.0°E
  RELEASES FILE:
    Point source at the top of the INTE building: 41.384° N, 2.116° E, 60 m a.g.l.
    Release start: 1 March 2007 9 UTC
    Release end: 1 March 2007 21 UTC
    Total mass: 21 kg of SO4 aerosol
    Particles released: 10000
Does all this make sense? What does this mean? Discuss results and test different output resolutions. The sync and average times. Number of particles.
Launch FLEXPART!
Notes: 5
5

## Slide 6
Hello World fwd & plotting
  Reflexible (evolution of pflexible) John Burkhart https://github.com/spectraphilic/reflexible
+ Python based
+ handle both binary and netcdf output
+ Easy folding with gridded inventories
+ ZAMG uses a variation of it operationally
+ Additional routines for dumping information and processing files (accumulate )
+ Simple plotting and complex plotting
  QuickLook
Based on flex_81.py
Under development
+ Easy command line parameters
+ Responsive developer
+ Python based
Radek Hofman https://bitbucket.org/radekhofman/quicklook/
Notes: 6
6

## Slide 7
Hello World fwd & plotting
Even some options for 3D plotting
  Matlab:
Requires license
Not fast
+ Easy folding with gridded inventories
+ nice 3D plotting capabilities
+ designed to deal with matrices
+ rendering possible
Sabine Eckhardt (NILU)
  plot_FLEX_binary.py
Very limited and developed for in-house use or testing
+ Free
+ Simple to use
+ Python based
Delia Arnold (ASC, ZAMG), Christian Maurer (ZAMG), Don Morton (Boreal SciCom)
Notes: 7
7

## Slide 8
Hello World fwd & plotting
Note there is the option of plotting the NetCDF output
https://www.giss.nasa.gov/tools/panoply/download/ PANOPLY(useful for Windows users)
http://meteora.ucsd.edu/~pierce/ncview_home_page.html NCVIEW
…
Notes: 8
8

## Slide 9
ECMWF: Hello World fwd & plotting
Results:
Did you get a ‘congratulations’ message on your run?
Yes  We should see the output produced
No  Were the option files well set? Was the compilation appropriate for your run? Is recompilation (with adjustment of par_mod.f90) needed?
./plot_FLEX_binary.py ./output_ECMWF/ False tracer1 0 0 alldates cyl False 0,20,37,44 mesh False
False – plot the MOTHER domain
Output directory
Species name
Level index (0: first level )
Release index (0: first release )
Dates to plot: „alldates“ or user-defined list of dates, e.g., 20170925000000,
20170925010000
Projection : Lambert or cylindric
No deposition plotted
Plotting region: left and right lon, lower and upper lat
Mesh or contour plotting
Add marked locations
Notes: 9
9

## Slide 10
ECMWF: Hello World fwd & plotting
Results:
Did you get a ‘congratulations’ message on your run?
Yes  We should see the output produced
No  Were the option files well set? Was the compilation appropriate for your run? Is recompilation (with adjustment of par_mod.f90) needed?
./plot_FLEX_binary.py ./output_ECMWF/ False 1 0 0 alldates cyl False 0,20,37,44 mesh False
./plot_FLEX_binary.py ./output_ECMWF/ True 1 0 0 alldates cyl True 1.0,4.3,40.0,43.8 mesh False
10000 particles
1000000 particles
Effect of number of particles…
Notes: 10
10

## Slide 11
NCEP: Hello World fwd & plotting
Results:
Did you get a ‘congratulations’ message on your run?
Yes  we should see the output produced
No  where the option files well set? Was the compilation appropriate for your run? Is recompilation (with adjustment of par_mod.f90) needed?
./plot_FLEX_binary.py ./output_NCEP/ False 1 0 0 alldates cyl False 0,20,37,44 mesh False
./plot_FLEX_binary.py ./output_NCEP/ True 1 0 0 alldates cyl True 1.0,4.3,40.0,43.8 mesh False
10000 particles
Notes: 11
11

## Slide 12
Hello World fwd & plotting
Results: plots of concentrations
What can we see?
Effect of OUTGRID resolution: Sharper and larger maxima, less smooth edges…
Notes: 12
12

## Slide 13
Hello World fwd & plotting
Results:
What can we see?
Effect of number of particles…
Notes: 13
13

## Slide 14
Another example: Output1 – 0.1 - 0.05 - 0.015
Hello World fwd & plotting
What does happen when resolution increases while keeping the number of particles ?

## Slide 15
Options:
Increase the number of particles  larger computational demands (FLEXPART 10 & FLEXPART-WRF are parallel/have option for a parallel executable) and the problem may appear later
Particle splitting  it increases the particles after a user-defined time-step. Number of particles increases exponentially and so do the computational times
Larger grid sizes (horizontal and vertical) so that more particles are sampled  smoothing
No perfect solution, trade-offs need to be made
Hello World fwd & plotting
What to do?

## Slide 16
ECMWF: Hello World fwd & plotting
Results: Concentration and deposition
What can we see?
Notes: 16
16